## Slide 1: NUMBER SYSTEM
PREPARED BY: ENGR. JAN REUELLE P. TEÑA

## Slide 2
Number Systems
Unary Numeral System
Binary Number System
Octal Number System
Hexadecimal Number System
Decimal Number System

## Slide 3
NUMBER SYSTEM
Number System is a set of values used to represent different quantities.

## Slide 4
UNARY NUMBER SYSTEM
One of the simplest numeral systems is the unary numeral system, in which every natural number is represented by a corresponding number of symbols.

## Slide 5: Decimal Number System
The Decimal Number System consists of ten digits from 0 to 9. These digits can be used to represent any numeric value. The base of decimal number system is 10. It is the most widely used number system. The value represented by individual digit depends on weight and position of the digit.

## Slide 6: Decimal Number System
Weightage of each position in Decimal Number System

## Slide 7: Binary Number System
Machine language is binary. This means that the machine language has binary values or two values, the combination of which represents the data. These two states are “on” state represented by 1 and “off” state, represented by “0”.

## Slide 8: Binary Number System
The binary number system is also a positional notation numbering system, but in this case, the base is not ten but is instead two

## Slide 9
Octal Number System
Octal number system uses numbers from 0 to 7 and the numbers are as a base of 8.

## Slide 10
Hexadecimal Number System
In Hexadecimal Number System the base used is 16. So there are 16 digits used to represent a given number.
The following are the hexadecimal numerals. 0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F; the number system is supplemented by letters as the base is greater than 10.

## Slide 11: CONVERSION ON NUMBER SYSTEMS

## Slide 12: BINARY TO DECIMAL BY POWER OF 2
It is the most straightforward method and is based on the positional notation of numbers. Starting from the right (the least significant bit) and moving left, each digit represents the next power of 2

## Slide 13: Binary Number System
25 | 24 | 23 | 22 | 21 | 20
32 | 16 | 8 | 4 | 2 | 1

## Slide 14: BINARY TO DECIMAL (Power of 2 Method)
Examples:
Convert 1010112 to Decimal
Convert 11011012 to Decimal

## Slide 15
Solution of Example 1 (Power of 2):
Given: Convert 1010112 to Decimal
Answer: 43
25 | 24 | 23 | 22 | 21 | 20
32 | 16 | 8 | 4 | 2 | 1
1 | 0 | 1 | 0 | 1 | 1

## Slide 16
Solution of Example 2 (Power of 2):
Given: Convert 11011012 to Decimal
Answer: 109
26 | 25 | 24 | 23 | 22 | 21 | 20
64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 1 | 0 | 1 | 1 | 0 | 1

## Slide 17: BINARY TO DECIMAL BY Doubling Method
It is a systematic technique that simplifies the conversion process of binary to decimal. It involves doubling a running total and adding binary digits one by one from left to right. Here's how it works:

## Slide 18: Steps Doubling Method
Start with a running total initialized to 0.
Begin with the leftmost (most significant) binary digit.
For each binary digit, double the running total and then add the value of the binary digit (0 or 1) to the total.
Move to the next binary digit to the right and repeat step 3.
Continue this process for all the binary digits, moving from left to right until you have processed all of them.
Once you've processed all the binary digits, the running total will be the equivalent decimal value.

## Slide 19: BINARY TO DECIMAL (DOUBLING METHOD)
Examples:
Convert 10101012 to Decimal
Convert 11110002 to Decimal

## Slide 20
Solution of Example 1 (Doubling Method):
Given: Convert 10101012 to Decimal
1 | 0 | 1 | 0 | 1 | 0 | 1
0 x 2 + 1 = 1
1 x 2 + 0 = 2
2 x 2 + 1 = 5
5 x 2 + 0 = 10
10 x 2 + 1 = 21
21 x 2 + 0 = 42
42 x 2 + 1 = 85
Answer: 85

## Slide 21
1 | 1 | 1 | 1 | 0 | 0 | 0
0 x 2 + 1 = 1
1 x 2 + 1 = 3
3 x 2 + 1 = 7
7 x 2 + 1 = 15
15 x 2 + 0 = 30
30 x 2 + 0 = 60
60 x 2 + 0 = 120
Answer: 120
Solution of Example 1 (Doubling Method):
Given: Convert 11110002 to Decimal

## Slide 22: BINARY TO OCTAL BY Binary grouping of bits (Sets of 3)
It is a process that involves grouping binary digits into sets of three, and then finding the octal equivalent for each group. This method leverages the fact that each octal digit can represent exactly three binary digits.

## Slide 23: Steps Binary grouping of bits (Sets of 3)
Start from the rightmost binary digit.
Group the binary digits into sets of three, starting from the right. If there are fewer than three digits in the leftmost group, you can add leading zeros to complete the group.

## Slide 24: Steps Binary grouping of bits (Sets of 3)
3. Convert each group of three binary digits into its octal equivalent using the following mapping:
Binary | Octal
000 | 0
001 | 1
010 | 2
011 | 3
100 | 4
101 | 5
110 | 6
111 | 7
4. Write down the octal digits for each group.
5. Combine the octal digits to form the octal equivalent of the entire binary number.

## Slide 25: BINARY TO OCTAL Binary grouping of bits (Sets of 3)
Examples:
Convert 100111002 to octal
Convert 1011000112 to octal

## Slide 26
1 | 0 | 0 | 1 | 1 | 1 | 0 | 0
4
3
2
Answer: 2348
Solution of Example 1 Binary grouping of bits (Sets of 3):
Given: Convert 100111002 to octal

## Slide 27
1 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1
3
4
5
Answer: 5438
Solution of Example 2 Binary grouping of bits (Sets of 3):
Given: Convert 1011000112 to octal

## Slide 28: BINARY TO HEX BY Binary grouping of bits (Sets of 4)
It is a process that involves grouping binary digits into sets of four (from right to
and finding their equivalent hexadecimal representation. Each group of four binary digits corresponds to a single hexadecimal digit. This method simplifies the conversion process because both the binary and hexadecimal systems are base-16, which means each hexadecimal digit can represent exactly four binary digits.

## Slide 29: Steps Binary grouping of bits (Sets of 4)
Group the binary digits into sets of four, starting from the right (the least significant bit). If there are fewer than four bits in the leftmost group, you can pad with leading zeros to create a group of four.

## Slide 30: Steps Binary grouping of bits (Sets of 4)
2. Convert each group of four binary digits into its equivalent hexadecimal digit using the following mapping:
Binary | Hex
0000 | 0
0001 | 1
0010 | 2
0011 | 3
0100 | 4
0101 | 5
0110 | 6
0111 | 7
1000 | 8
1001 | 9
1010 | A
1011 | B
1100 | C
1101 | D
1110 | E
1111 | F

## Slide 31: Steps Binary grouping of bits (Sets of 4)
3. Write down the hexadecimal digits for each group.
4. Combine the hexadecimal digits to get the hexadecimal representation of the entire binary number.

## Slide 32: BINARY TO HEXADECIMAL Binary grouping of bits (Sets of 4)
Examples:
Convert 1011111012 to hex
Convert 0100101012 to hex

## Slide 33
1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1
D
1
7
Answer: 17D16
Solution of Example 1 Binary grouping of bits (Sets of 4):
Given: Convert 1011111012 to hexadecimal

## Slide 34
0 | 1 | 0 | 0 | 1 | 0 | 1 | 0 | 1
5
0
9
Answer: 9516
Solution of Example 2 Binary grouping of bits (Sets of 4):
Given: Convert 0100101012 to hexadecimal

## Slide 35: BINARY(with Fractions) TO DECIMAL, OCTAL and HEXADECIMAL
Examples:
Convert 1101101.1012 to DEC, OCTAL, and HEX.,
Convert 1.1101102 to DEC, OCTAL, and HEX.,

## Slide 36
Solution of Example 1
Given: Convert 1101101.1012 to Decimal
Answer: 109.625
26 | 25 | 24 | 23 | 22 | 21 | 20 | . | 2-1 | 2-2 | 2-3
64 | 32 | 16 | 8 | 4 | 2 | 1 | . | 1/2 | 1/4 | 1/8
1 | 1 | 0 | 1 | 1 | 0 | 1 | . | 1 | 0 | 1

## Slide 37
Solution of Example 1
Given: Convert 1101101.1012 to Octal
1 | 1 | 0 | 1 | 1 | 0 | 1 | . | 1 | 0 | 1
5
5
5
1
Answer: 155. 58

## Slide 38
Solution of Example 1
Given: Convert 1101101.1012 to Hexadecimal
0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | . | 1 | 0 | 1 | 0
D
A
6
Answer: 6D. A16

## Slide 39
Solution of Example 1
Given: Convert 1.1101102 to Decimal
Answer: 1.8437510
20 | . | 2-1 | 2-2 | 2-3 | 2-4 | 2-5 | 2-6
1 | . | 1/2 | 1/4 | 1/8 | 1/16 | 1/32 | 1/64
1 | . | 1 | 0 | 1 | 1 | 1 | 1

## Slide 40
Solution of Example 1
Given: Convert 1.1101102 to Octal
 | 0 | 0 | 1 | . | 1 | 1 | 0 | 1 | 1 | 0
6
1
6
Answer: 1. 668

## Slide 41
Solution of Example 1
Given: Convert 1.1101102 to Hexadecimal
 | 0 | 0 | 0 | 1 | . | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
8
1
D
Answer: 1. D88

## Slide 42: DECIMAL TO BINARY (Continuous Division)

## Slide 43: DECIMAL TO BINARY (Continuous Division)
Examples:
Convert 97 to binary
Convert 123 to binary

## Slide 44
Solution of Example 1:
Given: Convert 97 to binary.
97
48
24
12
6
3
1
2
2
2
2
2
2
2
Remainders
1
1
0
0
0
0
1
Answer: 11000012

## Slide 45
123
61
30
15
7
3
1
2
2
2
2
2
2
2
Remainders
1
1
0
1
1
1
1
Answer: 11110112
Solution of Example 2:
Given: Convert 123 to binary.

## Slide 46: Descending Powers of Two and Subtraction

## Slide 47: DECIMAL TO BINARY Descending Powers of Two and Subtraction
Examples:
Convert 89 to binary
Convert 101 to binary

## Slide 48
26 | 25 | 24 | 23 | 22 | 21 | 20
64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 0 | 1 | 1 | 0 | 0 | 1
89 – 64 = 25
25 – 16 = 9
9 – 8 = 1
1- 1 = 0
Answer: 10110012
Solution of Example 1:
Given: Convert 89 to binary.

## Slide 49
26 | 25 | 24 | 23 | 22 | 21 | 20
64 | 32 | 16 | 8 | 4 | 2 | 1
1 | 1 | 0 | 0 | 1 | 0 | 1
101 – 64 = 37
37 – 32 = 5
5 – 4 = 1
1- 1 = 0
Answer: 11001012
Solution of Example 2:
Given: Convert 101 to binary.

## Slide 50: DECIMAL TO OCTAL (DIVISION BY MULTIPLES OF 8)
Examples:
Convert 78 to octal
Convert 350 to octal

## Slide 51
78 /64 = 1 remainder 14
14 /8 = 1 remainder 6
6/1 = 6 remainder 0
Answer: 1168
Solution of Example 1:
Given: Convert 78 to octal.

## Slide 52
350/64 = 5 remainder 30
30 /8 = 3 remainder 6
6/1 = 6 remainder 0
Answer: 5368
Solution of Example 2:
Given: Convert 350 to octal.

## Slide 53: DECIMAL TO OCTAL (Continuous Division)
Examples:
Convert 670 to octal
Convert 55 to octal

## Slide 54
670
83
10
1
8
8
8
8
Remainders
6
2
1
3
Answer: 12368
Solution of Example 1:
Given: Convert 670 to octal.

## Slide 55
55
6
8
8
Remainders
7
6
Answer: 678
Solution of Example 2:
Given: Convert 55 to octal.

## Slide 56: DECIMAL TO HEXADECIMAL (Continuous Division)
Examples:
Convert 455 to hexadecimal
Convert 849 to hexadecimal

## Slide 57
455
28
1
16
Remainders
7
1
12 = C
Answer: 1C716
16
16
Solution of Example 1:
Given: Convert 455 to hexadecimal.

## Slide 58
849
53
16
16
Remainders
1
5
Answer: 35116
3
16
3
Solution of Example 2:
Given: Convert 849 to hexadecimal.

## Slide 59: OCTAL TO BINARY Direct Octal to Binary Conversion" or "Octal to Binary Translation
Examples:
Convert 57438 to Binary
Convert 8498 to Binary

## Slide 60
1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1
5
7
4
3
Answer: 1011111000112
Solution of Example 1:
Given: Convert 57438 to binary.

## Slide 61
0 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 0
3
5
6
2
Answer: 0111011100102
Solution of Example 2:
Given: Convert 35628 to binary.

## Slide 62: OCTAL TO DECIMAL
Examples:
Convert 17328 to Decimal
Convert 3278 to Decimal

## Slide 63
PLACE | THOUSANDS | HUNDREDS | TENS | ONES
OCTAL | 1 | 7 | 3 | 2
MULTIPLIER | 83 | 82 | 81 | 80
EQUIVALENT | 512 | 64 | 8 | 1
(1x 83) + (7x 82)+ (3x 81)+ (2x 80) = (1 x 512) + (7 x 64) + (3 x 8) + (2 x 1) = 512 + 448 + 24 + 2
= 986
Answer: 98610
Solution of Example 1:
Given: Convert 17328 to Decimal.

## Slide 64
PLACE | HUNDREDS | TENS | ONES
OCTAL | 3 | 2 | 7
MULTIPLIER | 82 | 81 | 80
EQUIVALENT | 64 | 8 | 1
(3x 82) + (2x 81)+ (7x 80) = (3 x 64) + (2 x 8) + (7 x 1) = 192+ 16 + 7
= 215
Answer: 21510
Solution of Example 2:
Given: Convert 3278 to Decimal.

## Slide 65: OCTAL TO Hexadecimal
Examples:
Convert 4358 to Hexadecimal
Convert 3218 to Hexadecimal

## Slide 66
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 1
4
3
5
1 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 1
D
1
1
OCTAL TO BINARY
BINARY TO HEXADECIMAL
Answer: 11D16
Solution of Example 1:
Given: Convert 4358 to Hexadecimal.

## Slide 67
0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1
3
2
1
0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1
1
D
0
OCTAL TO BINARY
BINARY TO HEXADECIMAL
Answer: D116
Solution of Example 2:
Given: Convert 3218 to Hexadecimal.

## Slide 68: HEXADECIMAL TO BINARY
Examples:
Convert ABC16 to Binary
Convert BEC16 to Binary

## Slide 69
1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0
A
B
C
Answer: 1010101111002
Solution of Example 1:
Given: Convert ABC16 to Binary.

## Slide 70
1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0
B
E
C
Answer: 1011111011002
Solution of Example 2:
Given: Convert BEC16 to Binary.

## Slide 71: HEXADECIMAL TO DECIMAL
Examples:
Convert 1ACD16 to Decimal
Convert 4E916 to Decimal

## Slide 72
PLACE | THOUSANDS | HUNDREDS | TENS | ONES
HEX | 1 | 10 | 12 | 13
MULTIPLIER | 163 | 162 | 161 | 160
EQUIVALENT | 4096 | 256 | 16 | 1
(1x 163) + (10x 162)+ (12x 161)+ (13x 160) = (1 x 4096) + (10 x 256) + (12 x 16) + (13 x 1) = 4096 + 2560 + 192 + 13
= 6861
Answer: 686110
Solution of Example 1:
Given: Convert 1ACD16 to Decimal.

## Slide 73
PLACE | HUNDREDS | TENS | ONES
HEX | 4 | 14 | 9
MULTIPLIER | 162 | 161 | 160
EQUIVALENT | 256 | 16 | 1
(4 x 162)+ (14 x 161)+ (9 x 160) = (4 x 256) + (14 x 16) + (9 x 1) = 1024 + 224 + 9
= 1257
Answer: 125710
Solution of Example 2:
Given: Convert 4E916 to Decimal.

## Slide 74: HEXADECIMAL TO OCTAL
Examples:
Convert 43516 to Octal
Convert D316 to Octal

## Slide 75
0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1
4
3
5
5
0
2
HEXADECIMAL TO BINARY
BINARY TO OCTAL
Answer: 20658
Convert 43516 to Octal
6
Solution of Example 1:
Given: Convert 43516 to Octal.

## Slide 76
0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1
D
3
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 1
3
2
3
HEXADECIMAL TO BINARY
BINARY TO OCTAL
Answer: 3238
Solution of Example 2:
Given: Convert D316 to Octal.